IMX8MP-SOM-EVB
User Manual
document revision 2.0	www.olimex.com
# What is iMX8MP-SOM-EVB

iMX8MP-SOM-EVB is an expansion board for easier evaluation of iMX8MP-SOM system-on-module development board. It has:

- iMX8MP-SOM matching connectors
- Two Gigabit Ethernet connectors
- Two CAN transceivers
- HDMI output connector
- Power jack for 5V DC
- Two serial debug UARTs (for A53 and M7)
- Micro SD-card connector
- Flash module connector
- USB 3.0 hosts
- PCI Express 3.0 M.2 expansion slot (2280) for nVME
- Headphone 3.5mm connector
- Microphone 3.5 mm connector
- Reset button
- PWR button
- UEXT connector
- Two GPIO connectors
- Optional ARM JTAG connector
- Boot slide switch
- Industrial grade temperature range: (-45+85)C
- Dimensions: (155 x 102)mm
- Open-hardware design, all original design files available, design made with KiCAD
## Order codes for iMX8MP-SOM-EVB and accessories

iMX8MP-SOM-EVB	Expansion board for easy evaluation of iMX8MP-SOM which can be	used as reference design; requires SOM module iMX8MP-	SOM-4GB-IND

iMX8MP-SOM-4GB-IND	Main module with i.MX8 quad-core MIMX8ML8CVNKZAB, 4GB	LPDDR4, EEPROM, PMIC

MICRO-SD-16GB-CLASS10	Blank 16GB microSD card
USB-CARD-READER	USB card reader and writer
SY1505E	Power adapter 5V 3A
SY2005E	Power adapter 5V 5A
USB-SERIAL-F	Serial debug cable for console log
Flash-e32Gs16M	Plug-and-play eMMC and SPI memory expansion module
CABLE-HDMI-50CM	HDMI cable
USB-KEYBOARD-PS2	Mini keyboard
PWR-CABLE	Cable with free leads fitting the Olimex barrel jacks
UEXT modules	There are temperature, humidity, pressure, magnetic field, light	sensors. Modules with LCDs, LED matrix, Relays, Bluetooth,	Zigbee, WiFi, GSM, GPS, RFID, RTC, EKG, sensors and etc.
# HARDWARE
## iMX8MP-SOM-EVB layout

Flash module

MicroSD card

USB3 hosts

Reset Power Buttons

M.2 nVM slot

Power +5V

HDMI

CAN

Gigabit Ethernet
Audio

Boot
GPIO

UEXT
GPIO
Debug

Optional JTAG

## iMX8MP-SOM-EVB schematics

Latest PDF export of schematic is available at GitHub:

iMX8MP-SOM-EVB schematic PDF

All design files and sources are again available at the GitHub page of the device.

## iMX8MP-SOM-EVB connectors
### UEXT1 connector

### Micro_SD1 connector

### Buttons

### EXT1 header

### EXT2 header

### PCI 3.0 M.2 (2280) nVME

### Audio out
HEADPHONES1 jack is handled by ES8388 audio driver. It is currently not supported in the official Linux images.

### Audio in
MICROPHONE1 jack is handled by ES8388 audio driver. It is currently not supported in the official Linux images.

# SOFTWARE

You can find Olimex-maintained recommended images here:

# Recommended Olimage Linux images

It is recommended to start with the base Armbian image. The minimal Armbian image has no graphical user interface.

The software we provide and maintain for iMX8MP-SOM-EVB is the same as for the main board:

- Armbian-based Debian 12 “bookworm” images (base and minimal) with support for the main chip and most peripherals, like USB 3.0, GbE, NVMe M.2 slot, Flash-header slot, serial debug, HDMI output (+audio over HDMI), CAN, etc. Known software issues: Currently there is no support for the ES8388 audio driver, e.g. HEADPHONES1 and MICROPHONE1 jacks won’t work without additional software work (HDMI audio works ok).
- Buildroot setup

# Document Revision History
Revision 2.0 February 2025:
- removed misleading information about recommended LCD
- fixed links
- added info about Armbian-based Debian image

Revision 1.0 May 2024
- initial document release